P.O. Box 1198

Camarillo, CA  93011-1198

Phone: (805) 484-2454, FAX: (805) 383-5909

E-mail: hlee@flatmonitors.com

Websites:  www.flatmonitors.com and www.peizen.com

# Assembly Instructions for

# Q-2050-RK Rackmount Kit

# Tools needed:

- 11/32 socket wrench

- 3/8 socket wrench or crescent wrench

- No. 2 Philip screw driver

- Tie wrap tool

- Wire cutter, angle tipped is recommended.

Procedures:

- Remove the monitor from its stand by removing four metric screws from its stand.  Store the stand in the original box with its associated hardware.  In case of warranty service, you will need to put the monitor back into its original configuration.

- Spread the soft foam pad that comes with the packing material on a tabletop.

- Lay the monitor face down.  Then position the Q-2050-RK on the back of monitor.  This rackmount kit comes in a locked-hinge configuration for easy assembly.  This rackmount kit can accommodate a number of TFT LCD monitors from 15” up to 20.1”.

- Pick the best set of four holes to mount the monitor so that it will appear almost centered vertically.

- Insert one set of No. 8 lock washer, No. 8 flat washer, and 4 mm X 16 mm metric screw (or other lengths depending on the depth of thread of the monitor) into each of the four VESA mounting holes.  Then securely tighten all four screws.

- The cable clamps provided are used for tying down the power cable and the SVGA monitor cable.  Secure the cables with 5” tie wraps onto the cable clamps.

- Trim all tie wraps with a wire cutter.

- Use four black 10-32 screws with No. 10 nylon washers on the left to secure the rackmount assembly onto the left rail and two thumbscrews with white nylon washers to secure the monitor onto the right rail.

- Unscrew the two thumbscrews on the left and slide the hinge-locking plate to the right to clear the hinges.  Then unscrew the two thumbscrews on the right side to allow the assembled monitor to swing open.

CAUTION: When the monitor is swung open, be sure there is enough clearance for the monitor screen. After all, it is made of glass. Also, be sure to put on a CAUTION flag so that people won’t bump into it.

- Secure the power cable and SVGA cable behind the left rail with rubberized cable clamps.  Utilize the thread of the black screws behind the left rail.  Insert a clamp into each cable.  Then feed the clamp onto a black screw.  Then insert a No. 10 flat washer and a 10-32 hex nut over the clamp and tighten the hex nut with a 3/8” crescent wrench.  Bundle the cables together with 5” tie wraps, as shown below:

- To close, swing the monitor into the closed position.  Slide the hinge cover plate over the hinges.  Screw in two thumbscrews to lock the cover plate.  Then screw in two thumbscrews on right side to lock in the monitor.

- If you have any questions or comments, please call Harry Lee toll-free at 1-866-484-2454 or e-mail to hlee@flatmonitors.com.